## Slide 1: Indirect Wind-Field Estimation by UAV: Drone Simulation
Written By: Kunal Deshmukh
Advisor: Dr. Geordan Gutow

## Slide 2: Contents
Variation in Material Density
Variation in Propeller Diameter
Variation in Propeller Thrust Constant
Variation in Motor Time Constant
Variation in drag coefficient (Cd) in X-direction
Variation in drag coefficient (Cd) in Pitching direction

## Slide 3: Variation in Material Density

## Slide 4: Sensitivity of Drone Pitch to Material Density
The absolute pitch angle of the drone decreases with increase in the material density of the drone; for a given value of wind speed.
The absolute pitch angle of the drone increases, with an increase in the wind speed – for a given density of drone material.

## Slide 5: Sensitivity of Angular Velocity of Propeller 1 and Propeller 2 to Material Density
The absolute angular velocity of propeller 1 and 2 decreases with an increase in wind velocity.
However, the absolute angular velocity of propeller 1 and 2 increases, with an increase in material density.

## Slide 6: Sensitivity of Angular Velocity of Propeller 3 and Propeller 4 to Material Density
The absolute angular velocity of propeller 3 and 4 increases with an increase in wind velocity.
Also, the absolute angular velocity of propeller 3 and 4 increases, with an increase in material density.

## Slide 7: Sensitivity of Aerodynamic Drag on Propeller 1 and Propeller 2 to Material Density
The absolute value of drag force on blades of propeller 1 and 2 decreases with an increase in wind velocity.
However, the absolute drag force on propeller 1 and 2 increases, with an increase in material density.

## Slide 8: Sensitivity of Aerodynamic Drag on Propeller 3 and Propeller 4 to Material Density
The absolute value of drag force on blades of propeller 3 and 4 increases with an increase in wind velocity.
Also, the absolute drag of propeller 3 and 4 increases, with an increase in material density.

## Slide 9: Sensitivity of thrust produced by Propeller 1 and Propeller 2 to Material Density
The thrust force produced by propeller 1 and 2 decreases with an increase in wind velocity.
However, the thrust force required from propeller 1 and 2 increases, with an increase in material density.

## Slide 10: Sensitivity of Thrust produced by Propeller 1 and Propeller 2 to Material Density
The thrust force produced by propeller 3 and 4 increases with an increase in wind velocity.
Also, the the thrust force required from propeller 3 and 4 increases, with an increase in material density.

## Slide 11: Sensitivity of Current required by Motor 1 and Motor 2 to Material Density
The current required by motor 1 and motor 2, decreases with an increase in wind velocity.
However, the current required by motor 1 and motor 2 increases, with an increase in material density.

## Slide 12: Sensitivity of Current required by Motor 1 and Motor 2 to Material Density
The current required by motor 1 and motor 2, increases with an increase in wind velocity.
Also, the current required by motor 1 and motor 2 increases, with an increase in material density.

## Slide 13: Variation in Propeller Diameter

## Slide 14: Sensitivity of Drone Pitch to Propeller Diameter
The absolute pitch angle of the drone chassis increases with an increase in the wind speed.
However, the pitch angle of the drone chassis is not affected by the size of the diameter of its propellers.

## Slide 15: Sensitivity of Angular Velocity of Propeller 1 and 2 to the Propeller Diameter
The absolute angular velocity of propeller 1 and 2, decreases with an increase in wind velocity.
Also, the absolute angular velocity of propeller 1 and 2 decreases, with an increase in propeller diameter.

## Slide 16: Sensitivity of Angular Velocity of Propeller 3 and 4 to the Propeller Diameter
The absolute angular velocity of propeller 3 and 4, increases with an increase in wind velocity.
However, the absolute angular velocity of propeller 3 and 4 decreases, with an increase in propeller diameter.

## Slide 17: Sensitivity of Drag force on Propeller 1 and 2 to the Propeller Diameter
The absolute drag force on propeller 1 and 2, decreases with an increase in wind velocity.
However, the absolute drag force propeller 1 and 2 increases, with an increase in propeller diameter.

## Slide 18: Sensitivity of Drag force on Propeller 3 and 4 to the Propeller Diameter
The absolute drag force on propeller 3 and 4, increases with an increase in wind velocity.
Also, the absolute drag force on propeller 3 and 4 increases, with an increase in propeller diameter.

## Slide 19: Sensitivity Thrust force produced by Propeller 1 and 2 to the Propeller Diameter
The thrust produced by propeller 1 and 2, decreases with an increase in wind velocity.
The thrust required from propeller 1 and 2 remains unaffected by an increase in propeller diameter.

## Slide 20: Sensitivity of Thrust force produced by Propeller 3 and 4 to the Propeller Diameter
The thrust produced by propeller 3 and 4, increases with an increase in wind velocity.
However, the thrust required from propeller 3 and 4 remains unaffected by an increase in propeller diameter.

## Slide 21: Sensitivity of the Current required by Motor 1 and 2 to the Propeller Diameter
The current required by motor 1 and 2, decreases with an increase in wind velocity.
However, the current required by motor 1 and 2 decreases, with an increase in propeller diameter.
(except for the change in diameter from 0.3 to 0.32)

## Slide 22: Sensitivity of the current required by Motor 3 and 4 to the Propeller Diameter
The current required by motor 3 and 4, increases with an increase in wind velocity.
Also, the current required by motor 1 and 2 decreases, with an increase in propeller diameter.
(except for the change in diameter from 0.3 to 0.32)

## Slide 23: Variation in Propeller Thrust Constant

## Slide 24: Sensitivity of Drone Pitch to Propeller Thrust Constant
The absolute pitch angle of drone increases with an increase in wind speed.
However, the pitch angle of drone remains unaffected by an increase in propeller thrust constant.

## Slide 25: Sensitivity of Angular Velocity of Propeller 1 and 2 to Propeller Thrust Constant
The absolute angular velocity propeller 1 and 2, decreases with an increase in wind velocity.
Also, the absolute angular velocity of propeller 1 and 2, decreases with an increase in propeller thrust constant.

## Slide 26: Sensitivity of Angular Velocity of Propeller 3 and 4 to Propeller Thrust Constant
The absolute angular velocity propeller 3 and 4, increases with an increase in wind velocity.
However, the absolute angular velocity of propeller 3 and 4, decreases with an increase in propeller thrust constant.

## Slide 27: Sensitivity of Drag force on Propeller 1 and 2 to Propeller Thrust Constant
The absolute drag force on propeller 1 and 2, decreases with an increase in wind velocity.
The absolute drag force on propeller 1 and 2, also decreases with an increase in propeller thrust constant.

## Slide 28: Sensitivity of Drag force on Propeller 3 and 4 to Propeller Thrust Constant
The absolute drag force on propeller 3 and 4, increases with an increase in wind velocity.
However, the absolute drag force on propeller 3 and 4, decreases with an increase in propeller thrust constant.

## Slide 29: Sensitivity of Thrust produced by Propeller 1 and 2 to Propeller Thrust Constant
The thrust force produced by propeller 1 and 2, decreases with an increase in wind velocity.
However, the thrust force produced by propeller 1 and 2, remains unaffected by an increase in propeller thrust constant.

## Slide 30: Sensitivity of Thrust produced by Propeller 3 and 4 to Propeller Thrust Constant
The thrust force produced by propeller 3 and 4, increases with an increase in wind velocity.
Also, the thrust force produced by propeller 3 and 4, remains unaffected by an increase in propeller thrust constant.

## Slide 31: Sensitivity of Current required by Motor 1 and 2 to Propeller Thrust Constant
The current required by motor 1 and 2, decreases with an increase in wind velocity.
Also, the current required by motor 1 and 2, decreases with an increase in propeller thrust constant.

## Slide 32: Sensitivity of Current Required by Motor 1 and 2 to Propeller Thrust Constant
The current required by motor 1 and 2, increases with an increase in wind velocity.
However, the current required by motor 1 and 2, decreases with an increase in propeller thrust constant.

## Slide 33: Variation in Motor Time Constant

## Slide 39: Variation in Drag Coefficient Cd in Y-direction

## Slide 41: Variation of Drag Coefficient in Pitch Direction